Goodness of fit statistics

The computation of goodness of fit depends on:
- Digits set to infinity by default.
- Unlog true/false value.
- Fitted.data.set (fitted.well): This the fitted results of the well from <fit.model>. See the documentation for creating fitted.wells object for more information.

The computation first calculates the sum of squared residuals. The residuals model is evaluated using the measured and the fitted OD values (fitted.well). The measured OD is actually the data from the second column of fitted.well.

For the predicted OD is calculated using the well.eval function with no timepoints argument (NULL). The well.eval function takes the fitted.data.set (fitted.well) as parameter and evaluates estimated OD at any timepoints. The ouput is evaluated using the equation and parameters from fitted.well. If predicted.OD is not a number then the residuals model function will return NA, otherwise the difference between measured.OD and predicted.OD is returned. Based on the unlog value should the function decides to use log for the fitted.data.set or not.
After that, the variance of x and y of the measured timepoints are computed based on the first 2 columns of fitted.data.set (fitted.well). The function then finally returns the negative log(10) of the residual sum of squares divided by variance on either axis, rounded with a certain number of digits specified in the digit parameter, indicated by:

-log({s} over {x times y } )

Where:
- s = Residual sum of squares extracted from fitted.well
- x = x variance
- y = y variance