The computation of the proportion of the plateau reached.

This computation answers whether if the curve come close to the plataeu OD during the experiment.The computation of the plateau reach depends on:
- fitted.data.set: fitted.wells (Data of wells after the fitting process). For more information, see Fitted.wells.odt for documentation of how fitted.wells object is made.
- The cutoff value
- unlog: Whether OD values should be returned on the linear scale instead of log-transformed scale.

First, the plateau OD from fitted parameters are retrieved from the fitted.well dataset. If the retrieved value is not numeric, NA is returned. Otherwise, base on the unlog, if the unlog value is set to false then the plateau OD is the retrieved value. If the unlog value is set to true then the plateau OD is defined as:

round(e^x - const) - where x is the retrieved value.

Second, OD at inoculation from fitted parameters is calculated. The well.eval function takes the fitted.data.set (fitted.well) as parameter and evaluates estimated OD at any timepoints. The ouput is evaluated using the equation and parameters from fitted.well. if the return value is NULL, then NA is returned. Otherwise, return a rounded value of:

well.eval(fitted.well, 0) – const where 0 is indicates the beginning of the experiment (t = 0).

And finally, the OD at the end of experiment from fitted parameters is calculated. Again, using the well.eval function , if the return value is NULL, then NA is returned. Otherwise, return a rounded value of:

well.eval(fitted.well, max(times in fitted.well)) - const with unlog is the passed parameter.

If final is not NA and the plateau OD is equals to the OD at the end of experiment, this function will return TRUE. Otherwise, return a TRUE if:
{(e - i)} over {(p - i)} > c

Where
e the OD at the end of experiment
i the OD at inoculation
p the plateau OD
c the the cut off value