How the fitted.well object is created

- The well.array is created by reading an xlsx or csv raw data file.
- This raw data then is transformed and normalized. (using normalize.and.transform.R class). For documentation of this step, see NormalizeAndTransform.odt.
- After that, the output data is pre-fitted by analyzing the curve shapes. (using slope.analysis.R class). For documentation of this step, see Prefitted And Fit Model Data.odt.
- Since some parameters take part in the process of creating a fitted.well obbject are related to models, see the documentation of class.model for equations of each model.

The main task is fitting parameterized models to the collected data. (using fit.model.R object)
Parameters:
- Input.wells: a pre-fitted and normalized data. This is an R-array object.
- growth.model: objects of class model (class.model.R object)
- backup.growth.model: objects of class model (class.model.R object)
- fit.if.no.growth: should the function attempt to fit a well even if there was no growth detected? The default is False.

At first, the three following slots in input.wells are changed to NA or empty value: <model.name>, <fit.par>, <equation>.

Get the OD vs. time data from well and stored it as input.data.

The function skips a well if there is no growth in slot “curve.par”, if fit-no-growth option is toggled to false and if there are fewer than 5 data points left in the analysis.

The function then changes the column headers of input.data to the more general "Time" vs. "y" model. It then extracts the model formula from <growth.model> in slot "formula" of the well object.
Use the function from slot "guess" to calculate initial guesses for model parameters based on slope estimates in <input.well>.

Attempt to fit a nonlinear least squares model, which determine the nonlinear (weighted) least-squares estimates of the parameters of a nonlinear model.

If using a Richards 5 parameter model, report an error if the fitted value for c(??) is negative, if the baseline is below the plateau, or if the fitted theta is negative.

If no error was reported by the model fitting, report successful fit in slot "fit.info", add coefficients to slot "fit.par", add the model equation and name to slots "equation" and "growth.model.name".

If the model fitting returned an error, do the same thing as above except using the backup model.

If both models failed, report a failure to slot "fit.info." leave the other slots blank or NA.