GCAT documentation for calculating goodness of fit and the reached plateau

Overview: This paper documents how the goodness of fit and the reached plateau are calculated in GCAT. The paper also tries to analyze the content of each well object generated from GCAT for analysis. GCAT first reads in the raw data as xlsx or csv file. These files can be raw data such as single plate and its layout. GCAT then creates an array of wells that represents each well in the plate. This raw data array then is transformed and normalized. After that, the transformed and normalized data is pre-fitted by analyzing the curve shapes. Since some parameters take part in the process of creating a fitted.well obbject are related to models, see part D of the documentation for equations of each model.

Notation:
object: An R object.
<text> : a slot/column/value named text.
Function(): a function created in GCAT named “Function” for repetition use.
Code: Code generated from R.
$slot: A sub slot.

A. Documentation for well object before fitting data.
Objective: Review what are contained in a well R object and document several functions needed for fitting data. Creating a new well object in R only requires Time and OD vectors, which will fill slot <screen.data>.

I/ List of well's attributes:
- <position> - 3-member vector containing identifying information for the well: row (letters), column (numbers) and plate ID.
- <well.info> - a list containing strain and media names if provided.
- <screen.data> - a data frame with Time and raw OD values. This is the only slot that is filled upon creation of a well object. As different functions are run on the well the data frame gets filled with additional columns.
- <use.log> - a single logical value denoting whether to return log-transformed values when data is requested from the well.
- <norm> - a value to subtract from all OD values before returning data, filled by normalize.ODs() function in the transforming and normalizing step.
- <curve.par> - a list of parameters that denote whether the well is empty, whether it contains ODs indicating a viable culture, whether it tanks at a certain timepoint.
- <fit.info> - a message with info about whether the fit was successful, failed, or skipped.
- <add.info> - a message with info about whether jumps in OD were detected or removed, or if ODs were detected below the blank OD.
If model fitting in the applying model step is successful:
- <fit.par> - will be a list containing the fitted model parameters
- <equation> - will contain an expression for evaluating the successfully fitted model
- <model.name> - will contain the name of the successfully fit model

An example of content of a single plate with no layout well object acquired from R:

position	Well.info	Screen.data	Use.log	norm	Curve.par	Fit.par	equation	Model.name	Fit.info	Add.info

Slot "position":
        plate row col
"single - YPDAFEXglucoseTests_2-25-10" "H" "12"

Slot "well.info":
$Strain
[1] Unknown Strain
Levels: Unknown Strain

$Media
[1] Unknown Media
Levels: Unknown Media

Slot "screen.data":
     Time OD
1 -1 0.0572
2 0 0.0577

Slot "use.log":
logical(0)

Slot "norm":
numeric(0)

Slot "curve.par":
$empty.well
[1] FALSE

Slot "fit.par":
list()

Slot "equation":
expression()

Slot "model.name":
character(0)

Slot "fit.info":
character(0)

Slot "add.info":
character(0)

II/ Some misc functions to extract and transform information from well objects.
(This list only contains functions that take part in the procedure of fitting, finding goodness, and finding the reached plateau.)
data.from(): Receives a well object and 4 logical values: <remove>, <remove.tanking>, <raw.data>, and <na.rm>.
By default it returns a two-column data frame with time and OD (or log OD if the <use.log> slot is true in the object), after normalization to the value specified in <norm> slot.
  - With <remove> set to true the rows specified in the <remove> column of the <screen.data> slot are not returned.
  - With <remove.tanking> set to true all the rows after the <tanking.start> index are removed.
  - Setting <raw.data> to true overrides all these settings and just returns 2 columns with Time and Raw OD.

slopes(): Receives a well object and 3 logical values: <remove>, <remove.tanking>, and <na.rm>.
This function acts much like data.from() but gives a single vector containing the slope at each point. It also has a parameter allowing removal of NA values.

B/ How the fitted.well object is created
Parameters:
- Input.wells: a pre-fitted and normalized data. This is an R-array object.
- growth.model: objects of class model.
- backup.growth.model: objects of class model, serves as a backup model if the first model fail.
- <fit.if.no.growth>: should the function attempt to fit a well even if there was no growth detected? The default is False.

At first, the three following slots in <input.wells> are changed to NA or empty value: <model.name>, <fit.par>, <equation>.

Get the OD vs. time data from well and stored it as input.data. The function skips a well if there is no growth in slot <curve.par>, if <fit-no-growth> option is toggled to false and if there are fewer than 5 data points left in the analysis. The function then changes the column headers of input.data to the more general "Time" vs. "y" model. It then extracts the model formula from growth.model in slot <formula> of the well object. Use the function from slot <guess> to calculate initial guesses for model parameters based on slope estimates in input.well. Attempt to fit a nonlinear least squares model, which determine the nonlinear (weighted) least-squares estimates of the parameters of a nonlinear model. If using a Richards 5 parameter model, report an error if the fitted value for c (What is c here?) is negative, if the baseline is below the plateau, or if the fitted theta is negative. If no error was reported by the model fitting, report successful fit in slot <fit.info>, add coefficients to slot <fit.par>, add the model equation and name to slots <equation> and <growth.model.name>. If the model fitting returned an error, do the same thing as above except using the backup model. If both models failed, report a failure to slot <fit.info> leave the other slots blank or NA.

C/ How the raw data is normalized and transformed
The following procedures are performed:
1. Set all timepoints to active for now using "points.to.remove=0" argument with remove.points() and adds an extra column to the slot of each well in the well array, specifying which points to remove when data is retrieved from the well.
2. Remove specified timepoints across wells (use "points.to.remove=NULL" if no points to remove). The function remove.points() receives two parameters: input.well and points to be removed. At first, the procedure will copy the <Remove> column or create a new one if and only if it does not exist to the well. After that, check if the points argument if it is a logical vector or not, recycle it along the length of <Remove>. If points parameter is not a logical vector, try to separate positive and negative integers (What is he trying to do here?). If points contains only zeros, reset the <Remove> vector to all False. Finally, the procedure replaces the old <Remove> column with the copied (or newly created) <Remove> column.
3. Normalize ODs using specified method and adding a constant if desired and sets the <norm> slot of each well to a value to be subtracted from OD values whenever data is retrieved from the well. The function Normalize.ODs() receives input.well, normalize method, blank value and adding constant as parameters. Normally, the function will use the blank OD and set the blank OD (minus the constant to be added) to the "norm" slot of each well.

Transform ODs on the logarithmic scale, regardless of whether <use.log> is true, an extra column of log-transformed values is added to the each well object in the well.array. The <use.log> slot of each well is set instead to determine whether the transformed values will be returned when data is retrieved from the well. The procedure of transforming ODs is carried out in transform.ODs() function in normalize.and.transform class. The function adds a <log.OD> column to the <screen.data> slot of a well object with log-transformed data. It also checks to see if any of the raw OD values (before a certain timepoint) is below the blank OD. All the points from the analysis that fall below the blank value will be removed. Also, if any points fall below the blank value by more than 0.2 * const (an added-constant) and before the cutoff index, the well will be removed from the analysis. Now, the function will take the natural log of the rest of the OD values and stores each of these values in the newly created <log.OD> column.

The input.well will now have a new column <screen.data>. And the <log.OD> column is a part of <screen.data>.

D/ How the normalized data is pre-fitted and modeled
I/ Pre-fitting process:
After the wells input are normalized and transformed, these wells data are pre-fitted, in other words, the curve shapes are analyzed.
The slope is estimated at each timepoint and add a column to the "well.array" (wells objects) slot of each well with the local slope at each timepoint. These slopes then are checked for tanking and/or jumping behavior. The procedure fills the "curve.par" slot of each well with <tanking.start>, denoting the timepoint at which tanking starts (if none, value is NA) . After <tanking.start> (?) all points are removed using remove.points(). It will also fill the <jump.error> slot with a status message, and try to use an automated process to remove the erroneous points if <remove.jumps> is true (the default is false).
After that, the curves are checked for growth above cutoff. The procedure then fills the <curve.par> slot of each well with <no.growth>, denoting whether the well has no detectable growth. This finishes the pre-fitting procedure.
Remark: View the documentation for class.well.R for more information about what are contained in a well object.

II/ Model fitting:
Objective: Fit each well with the selected model and attempt to catch failed fittings with the backup model.
The function skips wells designated as <no.growth> above and fills the <fit.info> slot of each well with "success," "failed," or "skipped". If fit was successful, the <equation> and <model.name> slots will be filled with the relevant info for the successful model. The <fit.par> slot with fitted parameters will also be filled if fit is successful. The next part documents 3 models for fitting data in each well.

III/ Class.model.R
All of the models listed here share some parameters:
- growth rate : 2nd column in a well object (data frame)
- time : 1st column in a well object (data frame)
1/ Logistics 4-parameter model: Normally, there are only 3 parameters. The extra fourth parameter allows estimating the baseline.
- Min.index = the index of the minimum value in the growth column.
- Max.index = the index of the maximum value in the growth column.
- G50 = the half-way points between the min and the max value in the growth column
- g50 distance = a data frame of absolute values of the difference between each growth and g50.
- G50.index = the index of the mid-value g50 data frame.

Get the slopes at min, max, and half-way points. The highest positive slope is used as the halfway slope. With:
g50.slopes = slopes(g50)

Compute initial guess:
- a = the minimum value of growth column
- b = the maximum value of growth column
- t50 = the time value at g50.index
- th = (b – a) over (4g50.slopes )

logistic.f = y = a + {(b - a)} over {1 + func e^{(t50 - time) over {th}}}

The model will be created using the formula above and the set of parameters (a, b, t50, th) in which:
(a = a, b = b, t50 = t50 – 1, th = th)

2/ Richards 5-parameter model:

y = a + (b - a) times (1 + c times func e^{{t50 - Time} over {th}})^{{-1} over {c}}

Similarly, the model will be created using the formula above and the set of parameters
(a, b, t50, th, c) in which:
(a = a, b = b, t50 = t50 – 1, th = th, c = 1)

3/ Gompertz model: useful as a limitting case of Richards model when c = 0

y = a + {(b - a)} over {func e^{func e^{{(t50 - Time)} over {th} } } }

Then, the model is created using the formula above and the set of parameters is the same as logistics model's.

These models are for the task of fitting wells' raw data. They serve as alternative for others. In other words, if one of them fail to fit the data, then GCAT might try a back up model, which is selected by the user's choice.

E/ Goodness of fit statistics:
The computation of goodness of fit depends on:
- Digits set to infinity by default.
- Unlog true/false value.
- Fitted.data.set (fitted.well): This the fitted results of the well.
The computation first calculates the sum of squared residuals. The residuals model is evaluated using the measured and the fitted OD values. The measured OD is actually the data from the second column of fitted.well object.
The predicted OD is calculated using the well.eval() function with no timepoints argument. The well.eval function takes the fitted.data.set (fitted.well) as parameter and evaluates estimated OD at any timepoints. The ouput is evaluated using the equation and parameters from fitted.well. If <predicted.OD> is not a number then the residuals model function will return NA, otherwise the difference between <measured.OD> and <predicted.OD> is returned. Based on the unlog value should the function decides to use log for the fitted.data.set or not.
After that, the variance of (x and y) of the measured timepoints are computed based on the first 2 columns of fitted.data.set. As mentioned above, the second column of fitted.data.set is the measured OD. The first column of fitted.data.set is the time. The function then finally returns the negative log(10) of the residual sum of squares divided by variance on either axis, rounded with a certain number of digits specified in the digit parameter, indicated by:

-log({s} over {x times y } )

Where:
- s = Residual sum of squares extracted from fitted.well
- x = x variance
- y = y variance

F/ The computation of the proportion of the plateau reached.
This computation answers whether if the curve come close to the plataeu OD during the experiment. The computation of the plateau reach depends on:
- fitted.data.set
- The cutoff value
- unlog: Whether OD values should be returned on the linear scale instead of log-transformed scale.

First, the plateau OD from fitted parameters are retrieved from the fitted.well dataset. If the retrieved value is not numeric, NA is returned. Otherwise, base on the unlog, if the unlog value is set to false then the plateau OD is the retrieved value. If the unlog value is set to true then the plateau OD is defined as:
round(e^x - const) - where x is the retrieved value.

Second, the OD at inoculation from fitted parameters is calculated. The well.eval() function takes the fitted.data.set as parameter and evaluates estimated OD at any timepoints. The ouput is evaluated using the equation and parameters from fitted.well. If the return value is NULL, then NA is returned. Otherwise, return a rounded value of:

well.eval(fitted.well, 0) – const where 0 is indicates the beginning of the experiment (t = 0).

Finally, the OD at the end of experiment from fitted parameters is calculated. Again, using the well.eval() function , if the return value is NULL, then NA is returned. Otherwise, return a rounded value of:

well.eval(fitted.well, max(times in fitted.well)) - const with unlog is the passed parameter.

If final is not NA and the plateau OD is equals to the OD at the end of experiment, this function will return TRUE. Otherwise, return a TRUE if:

{(e - i)} over {(p - i)} > c

Where:
- e the OD at the end of experiment
- i the OD at inoculation
- p the plateau OD
- c the the cut off value

need a formula for reach = f(rawOD, predictedOD)
Surject reach = max(rawOD)/max(predicted.OD)